## Slide 1: Lecture 2.1: Wrapping up load prediction.
S. Bose, K. Alshehri
Electrical and Computer Engineering
University of Illinois at Urbana Champaign
ECE 398 BD: Making sense of big data.
Fall 2018.

## Slide 2: Using neural networks + what you learned in Part 1, we will cover:
Lab 11: Patterns in load, load prediction, effects of renewable supply.
Lab 12: Power flow equations, sensor measurements and bad data detection.
Lab 13: Virtual trading in NYISO’s markets
Lab 14-15: As time permits:
  Maintaining grid frequency
  Making sense of smart meter data
Office hours: Fri 1-2pm. Email me if you need to meet outside of that.

## Slide 3: Power Grid: Overview
source

## Slide 4: Why predict load?
Operational paradigm of the power system:
Predict, schedule, balance
Day-ahead market
Real-time market
Automatic generation control
Primary frequency control
Closer to time of energy delivery
Load prediction allows you to ensure the availability of generators:
Ones with low ramping capabilities must be scheduled forward. Think nuclear.
Ones with high ramping capabilities should have fuel available. Think natural gas.

## Slide 5: Independent System Operators
source
NYISO: http://www.nyiso.com/public/markets_operations/market_data/load_data/index.jsp
ERCOT: http://www.ercot.com/gridinfo/load/load_hist/
PJM: https://www.pjm.com/markets-and-operations/energy.aspx
ISONE: https://www.iso-ne.com/isoexpress/web/reports/load-and-demand
CAISO: http://www.caiso.com/TodaysOutlook/Pages/default.aspx
MISO: https://www.misoenergy.org/markets-and-operations/real-time-displays/

## Slide 6: Changing resource mix of electricity generation
Utility-scale annual additions to generation capacity by source
27GW capacity addition in 2016
Wind = 8.7 GW,
Solar = 7.7 GW,
Natural gas = 9 GW.
Distributed (rooftop) solar = 3.4GW
Utility-scale
Electricity generation by source
An excellent source of data: Energy Information Administration https://www.eia.gov/

## Slide 7: Integrating VRE in transmission systems (Images from NREL, Wikipedia)

## Slide 8: Rapid adoption of wind and solar
27GW utility scale capacity addition in 2016:
Wind = 8.7 GW, Solar = 7.7 GW, Natural gas = 9 GW.
+ Distributed (rooftop) solar = 3.4GW

## Slide 9: Variable renewable energy (VRE)
Uncertain: difficult to forecast in advance
Intermittent: exhibits unpredictable ramps
Non-dispatchable: output is largely uncontrollable
Wind generation
Solar generation
Power
Time of day
Time of day

## Slide 10: Predict, schedule, balance
Day-ahead market
Real-time market
Automatic generation control
Primary frequency control
Closer to time of energy delivery
Created using load data from NYISO and synthetic wind data from NREL.
Net demand = Demand – Renewable supply
Load v/s net load
Fessenden ‘18

## Slide 11: Look at current operating conditions
Some ISOs already offer visualizations of their operating conditions:
ERCOT:
http://www.ercot.com/content/cdr/html/CURRENT_DAYCOP_HSL.html?uniquenessFactor=1541692881440
CAISO:
http://www.caiso.com/TodaysOutlook/Pages/default.aspx
Items to pay attention to:
Difference between day-ahead and real-time wind prediction in Texas.
Net demand versus demand in California